LjunggrenAudio RYO Airtenuator
a floating passive attenuator

Dimensions
Length:	58mm
Width:	16mm
Depth:	floating (cables attached)

Weight:	???g

Current consumption
+12V rail	0.2mA
-12V rail	no -12V supply required
+5V rail	no +5V supply required

@ 10V signal +/-20% from the output jack

Basic specifications
total frequency controllable range	dc to 50+kHz
max input/output audio signal	20Vpp
CV input range	-10V to +10V

Max gain	n/a

Nominal impedances
Audio signal input:	50k +/-20%
Audio Signal output:	(variable impedance if used backwards)
CV input:	n/a