LjunggrenAudio RYO Ampmix
A 4-channel amplifying mixer in 8hp

Quickstart – what is the Ampmix and how do I get going?blank blank blank blank blank blank blank

An easy to build 4-channel amplifying mixer/attenuator with 2.0x gain (6dB) and 5.0V offset on each channel in an 8hp module. No calibration required.

Ampmix was designed as a handy CV mixer and processor with good precision, high input impedance and buffered outputs. It can even be upgraded for even better precision as described in the assembly manual. It will also work great with audio, including full gain giving some distortion possibilities or driving external gear.

Installation

To begin installation, please make sure that:
- you have a standard pinout eurorack bus board
- you have +12V and -12V power rails on that bus board [no +5V supply is required]
- the power rails are not overloaded

!!!Before installing this module disconnect the power from your system!!!

- Double check the polarity of the ribbon cable - The red stripe should be aligned with the -12V rail, on both the module and on the bus board

[we use shrouded headers but it's still possible a cable has been assembled with the stripe on the wrong side of the shroud so always double check!].

Also make sure when using busboards without shrouded headers that the pins aren't transposed a row vertically or horizontally – all pins should insert into holes on the cable.

Although we use both PTC fuses and schottky diodes to provide reverse polarity and excess current protection, we do not take any responsibility for damages caused by wrong power supply connection!

After you have connected everything, double checked it and ensured your case is closed such that no power lines can be touched by your hand or any stray cables drop into holes, turn on your system and test the module

The Ampmix Kit is a novice-friendly project, it is a low part-count, single-PCB build that only requires the most basic experience in PCB soldering and module assembly. blank blank blank blank blank.

It works as:
- 4 channel mixer,
- 1 attenuator + 3 channel mixer,
- 2 attenuators + 2 channel mixer, or,
- 4 attenuators.
(With up to 2.0x gain (6dB) on each channel.)

If you chain channels you can get greater gain. You can chain any combination of channels it doesn't have to be in the described order. blank blank blank blank blank blank blank
Patch signal to with Input to IN1, and OUT1 -> IN2, then OUT2 will have 4x gain (12dB) total.
Continuing with OUT2 -> IN3 then OUT3 will have 8x gain (18dB) total.
Finally, Continuing with OUT3 -> IN4, then OUT4 will have 16x gain (24dB) total.

An offset voltage is generated then normalled to the inputs of the 4 channels, giving them a maximum of 5V output each with knobs turned full clockwise (2.0x gain). Please note that these offsets will affect the mixing if the channel hasn't been patched on its input or output, so turning all unused channels fully counter-clockwise/left (off) is advisable for a clean mix.

The module can be used as a basic attenuator; by patching a signal to any channel and taking it's individual output as the out, whilst keeping gain between fully CCW and 50% as desired. Blank blank blank blank blank blank.

Dimensions
Height:	3U (128.5mm)
Width:	8HP (40.30mm)
Depth:	35mm (with power cable attached)

Weight:	???g

Current consumption
+12V rail	22mA
-12V rail	22mA
+5V rail	no +5V supply required

[There are small power variations between different vactrol and LED varieties. The option requiring least power is SR3 optocoupler paired with green limiter LEDs.]

Basic specifications
total frequency controllable range	dc to 50kHz
max input/output audio signal	20Vpp
CV input range	0V to +10V

Max gain	6dB (2.0x) gain per channel
24dB gain with all channels	daisy-chained

Nominal impedances
Audio signal input:	22k ohm
Audio Signal output:	in loop compensated
CV input:	n/a

Patch ideas:

Although uses of mixers in patch examples and ideas are found readily online and in some books, and similarly those familiar with using attenuators will be familiar with the basics, there are other less obvious ways to use the ampmix in patches in your modular rig:

below i've include some inspiring words to encourage other patches that might be tried; and, as ever, experiment – RYO modules are designed with all necessary protection and fail-safes so you can just start plugging in patch cables and see what happens!

Overdrive other modules;
many modules can be fed a hot signal to overdrive the input stage	giving a nice distortion or warm tonality – this is especially true	for VCAs, filters and some mixers.

Boost/attenuate less commonly varied signal;
not only commonplace signals like the main audio in an output chain	or the end output of a patch might need boosting if gain is low,	also try boosting as well as attenuating FM modulators, AM	modulators and other secondary waveforms in a patch so that the	resulting sound output from a carrier VCO/VCF/VCA is different.