LjunggrenAudio RYO NOR/OR
Discrete Resistor-Transistor Boolean Logic in 4hp

Dimensions
Height:	3U (128.5mm)
Width:	4HP (20mm)
Depth:	45mm (with power cable attached)

Weight:	???g

Current consumption
+12V rail	max 28mA (@10V input signal)*
-12V rail	0V
+5V rail	no +5V supply required

*(14mA @ 5V input signal)

Basic specifications
total frequency controllable range	dc to 50kHz
max input/output audio signal	20Vpp
CV input range	n/a

Max gain	n/a

Nominal impedances
Audio signal input:	100k ohm
Audio Signal output:	1k ohm
CV input:	n/a