LjunggrenAudio RYO PATHS
A Cycling Sequential Switch

Dimensions
Height:	3U (128.5mm)
Width:	8HP (40.30mm)
Depth:	46mm (with power cable attached)

Weight:	???g

Current consumption
+12V rail	30mA
-12V rail	8mA
+5V rail	no +5V supply required

Basic specifications
total frequency controllable range	dc to 50kHz
max input/output audio signal	20Vpp
CV input range	-10V to +10V

Max gain	n/a

Nominal impedances
Audio signal input:	430ohm
Audio Signal output:	430ohm
CV input:	22kohm