LjunggrenAudio RYO Penta
a compact 4hp 5 step sequencer

Dimensions
Height:	3U (128.5mm)
Width:	4HP (20mm)
Depth:	39mm (with power cable attached)

Weight:	???g

Current consumption
+12V rail	6mA
-12V rail	1mA
+5V rail	no +5V supply required

Basic specifications
total frequency controllable range	dc to 50kHz
max input/output audio signal	n/a
CV input range (calibrate to preference)	0V to +10V

Max gain	n/a

Nominal impedances
Audio signal input:	100kohm
Audio Signal output:	in loop compensated
CV input:	n/a