LjunggrenAudio RYO 3xVCA
a Triple linear VCA in 4hp

Quickstart – what is the 3xVCA and how do I get going? Blank blank blank blank

The 3xVCA is a simple and space-efficient voltage controlled amplifier for processing of control voltages as well as audio with precision and a good clean sound.

This module gives you no less than three fully independent DC coupled linear VCAs with very similar response between each VCA in the same module and between other modules of this type.

Installation

To begin installation, please make sure that:
- you have a standard pinout eurorack bus board
- you have +12V and -12V power rails on that bus board [no +5V supply is required]
- the power rails are not overloaded

!!!Before installing this module disconnect the power from your system!!!

- Double check the polarity of the ribbon cable - The red stripe should be aligned with the -12V rail, on both the module and on the bus board

[we use shrouded headers but it's still possible a cable has been assembled with the stripe on the wrong side of the shroud so always double check!].

Also make sure when using busboards without shrouded headers that the pins aren't transposed a row vertically or horizontally – all pins should insert into holes on the cable.

Although we use both PTC fuses and schottky diodes to provide reverse polarity and excess current protection, we do not take any responsibility for damages caused by wrong power supply connection!
After you have connected everything, double checked it and ensured your case is closed such that no power lines can be touched by your hand or any stray cables drop into holes, turn on your system and test the module

The 3xVCA, like the 2xVCX, uses LM13700 OTA ic's at it's core for precision control over cv's, clean sound with audio and low noisefloor; All the outputs are buffered to avoid voltage droop regardless of what cables/modules are following the 3xVCA in the chain.
The 3xVCA can be calibrated to be fully open at any control voltage upto the eurorack standard maximum of +10V, but by default it is set to +5V so giving more than 1.0x gain when receiving +8V Doepfer A100 eurorack envelope signals.

The 3xVCA is a novice-friendly project, it is a low part count build that only requires basic experience in PCB soldering and module assembly:

The 3xVCA is great for adding extra life and dynamics to CV modulations as well as for regular audio duties such as a good sounding Amplitude Modulation all the way thru the audio spectrum.

The module requires calibration in several steps, achieved precision depends on the precision of your multimeter. Although it can be calibrated for any input cv, instructions are only provided for either 5V or 8V CV. Assembled modules are calibrated to 1.00x gain (0dB) at 5.00V CV, that means 8.00V CV will give a 1.65x gain (4.35dB).

The amplifier has an a linear response to control voltages, but also detailed in the associated documentation is a very simple modification which allows the 3xVCA to become both linear and exponential by normalling the VCAs in a cascading fashion.

The amplifier accepts both DC and AC signals, from static offset cv's right past audio frequencies upto 50+kHz.

The module is split into 3 VCA submodules – it has one audio input, one audio output and a cv input for each VCA; If VCA initial is required, an external offset will have to be summed to the input cv signal and likewise if the input cv needs attenuation this will have to be achieved off-board.

Dimensions
Height:	3U [128.5mm],
Width:	4HP [20mm],
Depth:	51mm (with power cable attached)

Weight:	???g

Current consumption
+12V rail	26mA
-12V rail	21mA
+5V rail	no +5V supply required

Basic specifications
total frequency controllable range	dc to 50 kHz
max input/output audio signal	20 Vpp
CV input range (calibrate to preference)	0V to +10V max

Max gain	0dB gain @+5V present at CV in
+8V CV gives 1.65x gain (4.35dB)

Nominal impedances
Audio signal input:	100k ohm
Audio Signal output:	1k ohm
CV input:	100k ohm

Patch ideas:

Although uses of VCAs in patch examples and ideas are found readily online and in some books, and similarly those familiar with using distortion effects perhaps from the guitar pedal cultural background, there are many other less obvious ways to use the optodist in patches in your modular rig:

below i've include everything from some inspiring words to links and embedded videos and diagrams with popular modules used to perform necessary duties showing the patches that have been used in the videos; and, as ever, experiment – RYO modules are designed with all necessary protection and fail-safes so you can just start plugging in patch cables and see what happens!

Dynamic modulation of cv inputs;
many modules have cv inputs allowing modulation of various parameters,	and likewise, many modules generate Cvs which can be used as sources of	modulation.
Putting a VCA in the cv-path of this source/destination pair can	give a much more interesting and varied range of sounds and modulation	options by adding a time dependent element such that as your patch	progresses and flows the sounds that emerge are more varied and rich.
 Try putting a VCA in between any cv-source/destination you can	think of and modulate the VCA with an LFO, EG or Sequencer to make it	vary	as time passes.

Add extra dynamic control to audio outputs;
Try using an extra VCA in the audio path modulated by another EG, on	top of the	commonly used note volume EG/VCA combo to allow further	volume modulation by,	e.g. velocity data.

Insert patch ideas here;
This video published by Ben of divkidmusic.com:

DivKid breakdown of 3xVCA

shows the perks of it's signal normalling turning this triple linear	VCA into a versatile multi response VCA. The normalling is a	modification that we make to all assembled 3xVCAs and is detailed	in the associated documentation for all DIYers.