RYO Altered States
Dual State Variable Voltage Controlled Filter

Quickstart – what is the Altered States and how do I get going?

Altered States is a dual analog state variable filter in a 20hp module. The filter cores are 12db/oct and based around the clean and reliable 2164 Quad VCA chipset and offers full voltage control over cutoff frequency and resonance as well as individual outputs for each filter response, including a variable state output with manual as well as voltage control.

Installation

To begin installation, please make sure that:
- you have a standard pinout eurorack bus board
- you have +12V and -12V power rails on that bus board [no +5V supply is required]
- the power rails are not overloaded

!!!Before installing this module disconnect the power from your system!!!

- Double check the polarity of the ribbon cable - The red stripe should be aligned with the -12V rail, on both the module and on the bus board

[we use shrouded headers but it's still possible a cable has been assembled with the stripe on the wrong side of the shroud so always double check!].

Also make sure when using busboards without shrouded headers that the pins aren't transposed a row vertically or horizontally – all pins should insert into holes on the cable.

Although we use both PTC fuses and schottky diodes to provide reverse polarity and excess current protection, we do not take any responsibility for damages caused by wrong power supply connection!

After you have connected everything, double checked it and ensured your case is closed such that no power lines can be touched by your hand or any stray cables drop into holes, turn on your system and test the module.

The Altered States is a high skill-level project, it has a large parts count and multiple PCBs, and hence requires significantly more than basic experience in PCB soldering and module assembly:

The following explanations only describe one of the twin filters, but apply to both in an identical fashion. The only part of the module that isn't an exact copy between the two is the two shared toggle switches.

Controls:

- Frequency cutoff control knob
- Resonance amount control knob
- Frequency cutoff CV attenuverter knob
- Input level attenuator with overdrive knob
- Variable state control minishaft type
- Resonance amount CV attenuverter minishaft type

Inputs/Outputs:

- Filter audio input
- Frequency cutoff CV input
- Frequency cutoff 1V/O scaled input
- Resonance amount CV input
- Variable state CV input
- Variable state output (LP-Notch-HP)
- Lowpass output
- Bandpass output
- Highpass output

Shared:

- Also available are a toggle switches for Combine (links the filter B frequency cutoff controls to filter A),
- and serial or parallel input routing.

The module has a response to control voltages such that the CV sockets accept both DC signals and AC signals into the full audio range.

Altered States is a highly versatile dual filter; the input and resonance controls both have enough range to dial in anything from smooth and clean to harsh, overdriven and screaming resonant tones.

The cores are very stable and will give you around 5 octaves of 1V/O tracking sine wave self-oscillation; the LP, BP and HP outputs each have a different phased sine. The state outputs offer seamless fading between lowpass and highpass filter response, with an all-pass/notch response around 50% of the knob setting.

With voltage control available on frequency cutoff as well as on resonance and state outs, the Altered States is perfectly suited for the modular environment. The filter cores are 12db/oct based around the clean and reliable 2164 Quad VCA chipset.

Dimensions
Height:	3U [128.5mm],
Width:	20HP [101.30mm],
Depth:	45mm (with power cable attached)

Weight:	???g

Current consumption
+12V rail	112mA
-12V rail	106mA
+5V rail	no +5V supply required

Basic specifications
total frequency controllable range	dc to 50kHz
max input/output audio signal	20Vpp
CV input range	-10V to +10V

Max gain	n/a

Nominal impedances
Audio signal input:	100k ohm
Audio Signal output:	1k ohm
CV inpt:	200k ohm

Patch ideas:

Here's some ways to use the Altered States in patches in your modular rig:

below i've included some inspiring words to show patches that may help you get creative; and, as ever, experiment – RYO modules are designed with all necessary protection and fail-safes so you can just start plugging in patch cables and see what happens!

Patch idea:
try combining the different outputs as either unusual phase	shifters, using the all pass as a phase shifter or using the self	oscillating outputs combined too get unusual phase shift	combinations...

Weird control voltages:
try inserting the many different types of filtering in the feedback	path of a delay...

Insert patch ideas here;
lorem ipsum got no more patch ideas. lorem ipsum got no more patch	ideas. Lorem ipsum got no more patch ideas. lorem ipsum got no more	patch ideas. lorem Ipsum got no more patch ideas. lorem ipsum got no	more patch ideas. lorem ipsum got no more patch ideas. lorem ipsum	got no more patch ideas. lorem ipsum got no more patch ideas. lorem	ipsum got no more patch ideas. lorem ipsum got no more patch ideas.	lorem ipsum got no more patch ideas. lorem ipsum got no more patch	ideas. lorem ipsum got no more patch ideas.

Audio:
using multiple self oscillating sine outs as into a ring mod such as	RYO 2xVCX with offset and different outs of the filter into the two	inputs audio to get fantastic new audio effects – combinations of	different phase waveforms from the filter will help you to tune your	effect to perfection.