LjunggrenAudio RYO VC Sequencer:
Compact 8-step Voltage Controlled Sequencer

Dimensions
Height:	3U (128.5mm)
Width:	10HP (50.50mm)
Depth:	42mm (with power cable attached)

Weight:	???g

Current consumption
+12V rail	22mA (version 1.2 28mA)
-12V rail	11mA
+5V rail	no +5V supply required

Basic specifications
total frequency controllable range	dc to 100+ kHz
max input signal	0V to +10V
max output signal/audio signal	10Vpp (-5V to +5V)

Max gain:	n/a

Nominal impedances
Audio signal input:	100k ohm
Audio Signal output:	in loop compensated
CV input:	n/a