LjunggrenAudio RYO 3xVCA
a Triple linear VCA in 4hp

Dimensions
Height:	3U [128.5mm]
Width:	4HP [20mm]
Depth:	51mm (with power cable attached)

Weight:	???g

Current consumption
+12V rail	26mA
-12V rail	21mA
+5V rail	no +5V supply required

Basic specifications
total frequency controllable range	dc to 50kHz
max input/output audio signal	20Vpp
CV input range (calibrate to preference)	0V to +10V max

Max gain	0dB gain @+5V present at CV in
+8V CV gives 1.65x gain (4.35dB)

Nominal impedances
Audio signal input:	100k ohm
Audio Signal output:	1k ohm
CV input:	100k ohm